## Slide 1: Replacement and maintenance

## Slide 2: Introduction
A business firm uses several machine and equipment for operation.
It is an absolute necessity to maintain the equipment in good operating conditions with economical cost
If a firm wants to be in the same business competitively, it has to take decision on whether to replace the old equipment or to retain it by taking the cost of maintenance and operation into account.

## Slide 3: Reasons for replacement
There are two basic reasons for considering the replacement of an equipment—
  physical impairment of the various parts
  obsolescence of the equipment.
In either case, replacement is done if having a new equipment is more economical rather than continuing with the old one.
Old asset is called defender and new asset is called challenger.

## Slide 4: Maintenance and its types
Maintenance activity can be classified into two types:
preventive maintenance :
Preventive maintenance (PM) is the periodical inspection and service activities which are aimed to detect potential failures and perform minor adjustments or repairs which will prevent major operating problems in future.

## Slide 5: Maintenance and its types (contd)
Breakdown maintenance:
It is the repair which is generally done after the equipment has attained down state. It is often of an emergency nature.
Preventive maintenance will reduce such cost up to a point. Beyond that point, the cost of preventive maintenance will be more when compared to the breakdown maintenance cost.

## Slide 6: Total maintenance cost
The total cost, which is the sum of the preventive maintenance cost and the breakdown maintenance cost, will go on decreasing with an increase in the level of maintenance up to a point. Beyond that point, the total cost will start increasing. The level of maintenance corresponding to the minimum total cost is the optimal level of maintenance

## Slide 7: Cost components
Any asset will have the following cost components:
Capital recovery cost (average first cost), computed from the first cost (purchase price) of the machine.
Average operating and maintenance cost (O & M cost)
Total annual cost is the sum of capital recovery cost (average first cost) and average maintenance cost.

## Slide 8: economic life of asset
the capital recovery cost (average first cost) goes on decreasing with the life of the machine
The average operating and maintenance cost goes on increasing with the life of the machine.
From the beginning, the total cost continues to decrease up to a particular life and then it starts increasing.
The point where the total cost is minimum is called the economic life of the machine.

## Slide 9: Graphical representation

## Slide 10: Challenger vs Defender
Challenger is the cheapest among all new alternative assets available in the market.
Defender is the old existing asset, currently in service.
Defender is replaced with challenger if equated uniform annual cost (EUAC) of challenger is less than EUAC of defender

## Slide 11: Example 1
A firm is considering replacement of an equipment, whose first cost is Rs. 4,000 and the scrap value is negligible at the end of any year. Based on experience, it was found that the maintenance cost is zero during the first year and it increases by Rs. 200 every year thereafter.
When should the equipment be replaced?

## Slide 12: Solution 1
End of year | Maintenance cost (Rs.) | Summation of maintenance cost (Rs.) | Average cost of maintenance (Rs.) | Average first cost (Rs.) | Sum of average cost (Rs.)=(EUAC)= (Total annual cost)
(n) |  | ∑B | C/A | 4000/n | D+ E
A | B | C | D | E | F
1 | 0 | 0 | 0 | 4000 | 4000
2 | 200 | 200 | 100 | 2000 | 2100
3 | 400 | 600 | 200 | 1,333.33 | 1,533.33
4 | 600 | 1200 | 300 | 1000 | 1300
5 | 800 | 2000 | 400 | 800 | 1200
Ans: 6 | 1000 | 3000 | 500 | 666.67 | 1,166.67*
7 | 1200 | 4200 | 600 | 571.43 | 1,171.43

## Slide 13: Example 2
A firm is considering replacement of an equipment, whose first cost is Rs. 1,750 and the scrap value is negligible at any year. Based on experience, it was found that the maintenance cost is zero during the first year and it increases by Rs. 100 every year thereafter.
When should the equipment be replaced if i = 0%?

## Slide 14: Solution 2
End of year | Maintenance cost (Rs.) | Summation of maintenance cost (Rs.) | Average cost of maintenance (Rs.) | Average first cost (Rs.) | Sum of average cost (Rs.)
(n) |  | ∑B | C/A | 1750/A | D+ E
A | B | C | D | E | F
1 | 0 | 0 | 0 | 1750 | 1750
2 | 100 | 100 | 50 | 875 | 925
3 | 200 | 300 | 100 | 583.33 | 683.33
4 | 300 | 600 | 150 | 437.5 | 587.5
5 | 400 | 1000 | 200 | 350 | 550
6 | 500 | 1500 | 250 | 291.67 | 541.67
7 | 600 | 2100 | 300 | 250 | 550

## Slide 15: Example 3 If Initial cost = Rs. 60,000, find the year in which the machine should be replaced .
Year | 1 | 2 | 3 | 4 | 5
Resale value ( Rs.) | 42,000 | 30,000 | 20,400 | 14,400 | 9,650
Maintenance cost. (Rs.) | 18,000 | 20,270 | 22,880 | 26,700 | 31,800

## Slide 16
Year n (1) | Maintenane Cost R(n) (2) | Cumulative maintenance Cost ΣR(n) (3) | Average maintenance cost (4) | Resale Value S (5) | Annual Depreciation Cost(CRC) Sn-1-Sn (6) | Average Total Cost ATCn (7) = 6+4
1 | 18,000 | 18,000 | 18000 | 42,000 | (60,000-42,000=) 18,000 | 36,000
2 | 20,270 | 38,270 | 19135 | 30,000 | (42,000-30,000=) 12000 | 31135
3 | 22,800 | 61,150 | 20383 | 20,400 | 9600 | 29983
4 | 26,700 | 87,850 | 21962 | 14,400 | 6000 | 27962*
5 | 31,800 | 119,650 | 23930 | 9,650 | 4750 | 28680